## Slide 1: Comparison of Methods for Capturing Material Discontinuities
Sean Davis and Will Matern
With an Introduction to GPU Programming

## Slide 2: Acknowledgements
Mentor: Dr. Bob Robey
Workshop Coordinator: Dr. Scott Runnels
Collaborator: David Nicholaeff
Thank you!

## Slide 3: Outline
Motivation
Discontinuities
Problems observed in numerical methods
Description of methods reviewed
  Lax-Wendroff with limiters
  MPDATA
  MUSCL
  SUPG
Results
  2D Advection Equations
GPU Programming
Conclusions

## Slide 4: Motivation
A simple model problem showing the advection of radioactive

## Slide 5: Contact discontinuities
A discontinuity that occurs in density but other quantities like pressure, velocity, and specific internal energy are continuous.
From Harlow and Amsden - “Fluid Dynamics”

## Slide 6: Problems observed in numerical methods for equations with discontinuities
Oscillations – High Order schemes
  Ex) Lax-Wendroff
Large dissipation – First Order Schemes

## Slide 7: CFL condition
Related to information propagation.
  Numerical solution should not move faster than analytic.
  This means:
For some methods CFL = 1 means a perfect propagation speed.
  Easy proof that Lax-Wendroff and Upwind converge to the exact solution when CFL =1.

## Slide 8: Descriptions of methods reviewed
Lax-Wendroff w/o Limiters
  Conservative 2nd order scheme
  Approximate solution has oscillations around sharp gradients

## Slide 9: Description of methods reviewed
Lax-Wendroff w/ Limiters
  1st order near discontinuities, 2nd order elsewhere
  For linear equations is mathematically guaranteed to be TVD

## Slide 10: Description of methods reviewed
MUSCL
  ACM – Slope limiter method for sharpening discontinuities.

## Slide 11: Description of methods reviewed
Streamline Upwind Petrov-Galerkin (SUPG)
  Finite Element approach
  Inspired by finite difference methods (upwinding and artificial diffusion)
  Applies to linear advection/diffusion equations of any dimension
  Is neither TVD nor conservative

## Slide 12: Theory of the Streamline Upwind Petrov-Galerkin (SUPG)
Trial functions – a set of functions assumed to approximate the underlying solution. The trial functions have degrees of freedom that must be solved for.
Test functions – a set of functions used to solve for the degrees of freedom of the trial functions. Uses the weak formulation of the governing equation.
Petrov-Galerkin – Test functions ≠ Trial functions
SUPG – Choose test functions to be:
where N is a trial function

## Slide 13: Results for 1D Advection in a 2D Code after 10 Periods
Lax-Wendroff (not TVD):
Lax-Wendroff (Superbee):
MUSCL:
SUPG:
Notes: Only show the last column.

## Slide 14: 2D Wave Advection Test Conclusions
Lax-Wendroff with slope limiters
  Effective for sharp discontinuities
  Overly dissipative for thin waves (cuts off the top of the triangular/gaussian waves)
  more dissipative than other methods
MUSCL with ACM
  most effective for problems with discontinuities
  Unnaturally sharpens the solution
SUPG
  Balances well between diffusion and discontinuity sharpness
  Doesn’t introduce unnatural sharpening
  Requires matrix operations
  Non-conservative

## Slide 15: Derivation of Lax-Wendroff for advection equation
Advection Equation:
Note that:
Replace the first two time derivatives with spatial derivatives
Remove 3rd order terms and above, and use central difference formulas:

## Slide 16: Limiters
Godunov’s Theorem – Any linear scheme above first order accurate (space) cannot be Total Variation Diminishing (TVD).
First order methods – often lead to large numerical diffusion
Solution: Limiters (a nonlinear scheme)
  First order at discontinuities
  Higher order where solution is smooth
  For certain linear problems can be shown to be TVD.

## Slide 17: MPDATA - Derivation
MPDATA
  One-sided bias donor cell approach
  Using a modified equation analysis, find an extra diffusive term
  Subtract out diffusive error using an anti-diffusive velocity

## Slide 18: MPDATA - Conclusions
MPDATA
  Options to control total variation (FCT) and

## Slide 19: GPUs at a glance
Much higher FLOPS (floating points operations per second) per dollar than CPUs.
Different architecture from a CPU.
  Many low throughput processing units
  Cores on the same card have shared global memory
  Warp/Wavefront- Similar to vector processor except much larger (SIMD)
Must use a language compiled for GPU
  OpenCL – Open programming language that can make use of multiple CPUs (on the same node) and a GPU. Can combine with MPI for multiple nodes.
  CUDA – Nvidia only.
This Project: OpenCL

## Slide 20: GPU architecture
Global Memory
  Available to entire device
Local Memory
  Available to the work group only
  ***I think this isn’t well defined in OpenCL and can spill over to Global without warning
Private Memory
  Available to work item only
Constant Memory
  Read only, can be faster than global
SIMD group size – efficient code is a multiple of this
  Nvidia – Warp = 32 cores
  ATI – Wavefront = 64 cores
  http://stackoverflow.com/questions/7093488/opencl-how-to-i-query-for-a-devices-simd-width

## Slide 21: Shallow Water Equations
Simplification of the Euler Equations
  Uniform Fluid Density
  Wavelengths are much longer than fluid depth
  Inert Tracer Equation

## Slide 22: Shallow Water Simulations on the GPU
Fluid Height
Inert Tracer Concentration

## Slide 23: Future Directions
FEM approach for full Euler equations
Implement schemes for advection on the GPU (include in CLAMR)
Implement these schemes to solve the full Euler Equations
Alternative numerical methods (WENO, Discontinuous Galerkin, etc.)

## Slide 24: Question, Comments, Suggestions?