## Slide 1: Comparison of Methods for Capturing Material Discontinuities
Sean Davis and Will Matern
With an Introduction to GPU Programming

## Slide 2: Acknowledgements
Mentor: Dr. Bob Robey
Workshop Coordinator: Dr. Scott Runnels
Collaborator: David Nicholaeff
Thank you!

## Slide 3: Outline
Motivation
Problems with capturing discontinuities
Methods implemented and tested
  First order Upwind
  Lax-Wendroff with limiters
  MUSCL
  SUPG
Early MPDATA results
GPU Programming
  Introduction
  Results solving the shallow water equations
Conclusions

## Slide 4: Motivation
A simple model problem showing the advection of radioactive water dumped into the ocean and carried by a rotational current across the Pacific.

## Slide 5: First Order Upwind Scheme
Conservative 1st order scheme
Overly dissipative

## Slide 6: Lax-Wendroff w/o Limiters
Conservative 2nd order scheme
Approximate solution has oscillations around sharp gradients

## Slide 7: Limiters
Godunov’s Theorem – Any linear scheme above first order accurate (space) cannot be Total Variation Diminishing (TVD).
Solution: Limiters (a nonlinear scheme)
Exact Solution
Non-TVD Solution
Notes: First order at discontinuities
Doesn’t affect the solution when it is smooth
Discuss TVD

## Slide 8: Lax-Wendroff w/ Superbee Limiter
1st order near discontinuities, 2nd order elsewhere
For linear equations is mathematically guaranteed to be TVD

## Slide 9: Monotone Upstream Scheme for Conservation Laws (MUSCL)
Used a modified Osher-Chakravarthy scheme [10]
Second order TVD approximation
Upwind biased
Numerical oscillations avoided using a minmod function

## Slide 10: Streamline Upwind Petrov-Galerkin (SUPG)
Trial functions – a set of functions assumed to approximate the underlying solution. The trial functions have degrees of freedom that must be solved for.
Test functions – a set of functions used to solve for the degrees of freedom of the trial functions. Uses the weak formulation of the governing equation.
Petrov-Galerkin – Test functions ≠ Trial functions
SUPG – Choose test functions to be:
where N is a trial function

## Slide 11: SUPG
Finite Element approach
Inspired by finite difference methods (upwinding and artificial diffusion)
Applies to linear advection/diffusion equations of any dimension
Is neither TVD nor conservative

## Slide 12: Wave Advection Test Conclusions
Lax-Wendroff with slope limiters
  Effective for sharp discontinuities
  Overly dissipative for thin waves (cuts off the top of the triangular/gaussian waves)
  more dissipative than other methods
  Superbee limiter artificially sharpens smooth waves
MUSCL with ACM
  most effective for problems with discontinuities
  Unnaturally sharpens the solution
SUPG
  Balances well between diffusion and discontinuity sharpness
  Doesn’t introduce unnatural sharpening
  Requires matrix operations
  Non-conservative

## Slide 13: Results for 1D Advection in a 2D Code after 10 Periods
Lax-Wendroff (not TVD):
Lax-Wendroff (Superbee):
MUSCL:
SUPG:
Notes: Only show the last column.

## Slide 14: Multidimensional Positive Definite Advection Transport Algorithm (MPDATA)
A donor-cell approximation is defined in terms of the local Courant number
Adds a diffusive convective flux
Subtract out added dissipation using an antidiffusive velocity
As an example, the 1D advection equation,
becomes,
Notes: Using a modified equation analysis.

## Slide 15: MPDATA
Antidiffusive correction to the donor cell method causes oscillations
PRELIMINARY

## Slide 16: MPDATA
A Flux Corrected Transport (FCT) algorithm can correct the oscillations
Performing additional local corrective iterations increases the order of accuracy of the solution
PRELIMINARY

## Slide 17: GPUs at a glance
Different architecture from a CPU.
  Many low throughput processing units
  Cores all share memory
  Workgroups
Higher FLOPS (floating points operations per second) per dollar than CPUs.
Must use a language compiled for GPU
  OpenCL – Open programming language that can make use of multiple CPUs (on the same node) and a GPU. Can combine with MPI for multiple nodes.
  CUDA – Nvidia only.

## Slide 18: GPU architecture
Global Memory
  Available to entire device
Local Memory
  Available to the work group only
  ***I think this isn’t well defined in OpenCL and can spill over to Global without warning
Private Memory
  Available to work item only
Constant Memory
  Read only, can be faster than global
SIMD group size – efficient code is a multiple of this
  Nvidia – Warp size is 32
  ATI – Workgroup size is 64
  http://stackoverflow.com/questions/7093488/opencl-how-to-i-query-for-a-devices-simd-width

## Slide 19: Shallow Water Equations
Simplification of the Euler Equations
  Uniform Fluid Density
  Wavelengths are much longer than fluid depth
  Inert Tracer Equation
Notes: Talk about the simplifications and that the tracer equation is simply an advection equation.

## Slide 20: Shallow Water Simulations on the GPU
Fluid Height
Inert Tracer Concentration

## Slide 21: Future Directions
FEM approach for full Euler equations
Implement more of these schemes in the GPU code
Develop full Euler Equation solvers with some of these schemes
Alternative numerical methods (WENO, Discontinuous Galerkin, etc.)

## Slide 22: Question, Comments, Suggestions?